## Slide 1: Title Slide
Sliding Mode Control for Power-Based Transparency Optimization in Admittance Control
Enhancing Human-Robot Interaction via Energy-Aware Damping Adaptation

## Slide 2: Motivation
- In physical human-robot interaction (pHRI), maximizing transparency is essential for intuitive and responsive control.
- Transparency: the degree to which the robot follows the user's motion without adding perceived resistance.
- Purpose: Explore if we can maintain high transparency while ensuring system stability and passivity.

## Slide 3: Why This Matters
- Standard admittance control uses a fixed mass-damper model:
M x_ddot + B(t) x_dot = F_h
- High damping ensures stability but limits responsiveness.
- Need a method to adaptively tune damping to maximize transparency without compromising safety.

## Slide 4: Why Choose Sliding Mode Control?
- Sliding mode control (SMC) ensures convergence to desired system behavior even under uncertainty.
- It provides a robust way to define a control objective (sliding surface) and force the system to follow it.
- Ideal for regulating energy exchange via damping in a human-in-the-loop system.

## Slide 5: Basic Idea of Sliding Mode Control
- Define a surface S(x, x_dot) representing desired energy behavior.
- Use a reaching law to drive S → 0.
- When S = 0, the system behaves optimally with respect to the control goal.
- We define S = F_h ⋅ x_dot - P_0, where P_0 is a small target power level.

## Slide 6: Power Flow Captures Human Intention
- Power P_h = F_h ⋅ x_dot reflects the interaction:
  - Positive: user wants to move the robot
  - Negative: user wants to resist motion
- Using P_h allows adaptive damping in sync with human intent.

## Slide 7: Designing the Sliding Surface
- Define: S = P_h - P_0 = F_h ⋅ x_dot - P_0
- Interpretation:
  - S > 0 → reduce damping to promote motion
  - S < 0 → increase damping to resist motion
- Goal: Keep P_h ≈ P_0 for high transparency.

## Slide 8: Reaching Law and Convergence
- Control input: damping B(t)
- Reaching law: dot{B}(t) = -k S(t)
- System dynamics: x_ddot = (F_h - B(t) x_dot)/M
- As B(t) adapts via S(t), the power converges toward P_0, ensuring transparency.

## Slide 9: Simulation Highlights
- At low velocities, damping remains high to avoid sudden motion.
- When motion is detected, damping adapts to match power with P_0.
- Ensures stable yet responsive behavior without violating passivity.

## Slide 10: Further Steps
- Extend to multi-DOF robotic manipulators
- Integrate with intent estimation from force and motion profiles
- Explore adaptive and bounded control laws for dot{B}(t)
- Formalize results for potential publication (e.g., ICRA, TRO)

## Slide 11: Thank You
Questions & Discussion